Update ONU Firmware from Uboot

If the ONU system fimware is damaged during firmware updating and cause system can not strat normally, then you need to resconvert system firmware from the Uboot.

Step1:Connect PC and issue ONU as following:

Step2: Connect serial line as following

Step3: Run Hyper Terminal and configure as following:

Step4: Run the TFTP server tool “tftpd32.exe” as following

Step5: Copy the ONU new firmware to the directory of tftpd32

Step6: ONU power on, and press “2” when you see the following output prompt:

Step7: Input “y”, and then change device IP address and TFTP server IP, and input firmware name.

Step8: ONU start to download firmware from TFTP server, and then erase FLASH and copy firmware to FLASH.

Step9: After write firmware to FLASH successfully, ONU will reboot automatically.

END.